TEXT BLOCK

ASSMANN DIGITUS DK-1641-A-xxx Premium CAT 6A S-FTP Patch Cable

SPECIFICATIONS

------------------------------------------------------------------------------

OZ       Specification of Services                 Unit Price      Total Price

------------------------------------------------------------------------------

-.-.-	Composition:

Copper Patch Cable Category 6A shielded (4x2xAWG26/27) for structured building cabling according to EN 50173-1:2002, ISO/IEC 11801:2002-9

- 2xRJ45 Connector

- 4x2 AWG 26/7, Twisted Pair

- Hoods with kink protection and strain relief

- Length designation on the hood

- Type CM (UL) C (UL) CMH E222711-F3 3P/ETL Verified

- Shielding: S-FTP, pairs shielded in metal foil and braid

- Cable Design: 4x2 AWG 26/7, Twisted Pair

- FR/PVC Cable Sheathing

- Length: 0.5; 1.0; 2.0; 3.0; 4.0; 5.0; 7.0; 10.0; 20.0 meters

- Color: gray

- Allocation: 1:1

Product: DIGITUS

Type: DIGITUS Premium CAT 6 S-FTP Patch Cable

Item no. DK-1641-A-xxx

or equivalent. When submitting a tender, the bidder has

to prove the equivalence by submitting the corresponding

data sheets/certificates from an independent testing institute:

Make/type offered:

Materials:............EUR

Wages    :............EUR

Fully delivered and installed

Piece              ...........EUR     ...........EUR