TEXT BLOCK

ASSMANN DIGITUS DK-1643-A-xxx Premium CAT 6A S-FTP Patch Cable

SPECIFICATIONS

------------------------------------------------------------------------------

OZ       Specification of Services                 Unit Price      Total Price

------------------------------------------------------------------------------

-.-.-	Composition:

Copper Patch Cable Category 6A shielded (4x2xAWG27/7) for structured building cabling according to EN 50173-1:2002, ISO/IEC 11801:2002-9

- 2xRJ45-TM21-88P Connector

- 4x2 AWG 27/7, Twisted Pair S-FTP (PiMF)

- Hoods with kink and snag protection and splashed strain relief

- Length designation on the cable sheathing

- Shielding: S-FTP, pairs shielded in metal foil and braid

- Cable Design: 4x2 AWG 27/7, Twisted Pair

- FR/PUR IEC 60332-1 Cable Sheathing

- UV – resistance of the sheathing material according to IEC60068-2-5

- Smoke gas density according to EN 50268-2, IEC61034-1 and 2

- Halogen-free according to EN 50267-1 and 2,IEC 60754-1 and 2

- Bending radii without tensile load ≥ 25 mm; with tensile load ≥ 50 mm

- Length: 0.5; 1.0; 2.0; 3.0; 4.0; 5.0; 7.0; 10.0; 20.0 meters

- Color: gray, blue, green, red, yellow

- Color of cable sheathing and kink protection hood are identical

- Allocation: 1:1

Product: DIGITUS

Type: DIGITUS Premium CAT 6 S-FTP Patch Cable

Item no. DK-1643-A-xxx

or equivalent. When submitting a tender, the bidder has

to prove the equivalence by submitting the corresponding

data sheets/certificates from an independent testing institute:

Make/type offered:

Materials:............EUR

Wages    :............EUR

Fully delivered and installed

Piece              ...........EUR     ...........EUR