TEXT BLOCK

ASSMANN DIGITUS Data Cable, DK-1741-VH-xxx, 4x2x23# S/FTP Category 7 100 Ohm LS0H Data Cable

SPECIFICATIONS

------------------------------------------------------------------------------

OZ       Specification of Services                 Unit Price      Total Price

------------------------------------------------------------------------------

-.-.-	Composition:

Conductor:				bare copper wire, AWG 23/1

Isolation:				SFS-PO, Wire-Ø: 1.6 mm nominal value

Stranding element:			pair

Individual shield:			Aluminum-laminated polyester film, metal side

outside (PiMF)

Stranding:				4 pairs

Overall shield:			tin-plated copper braid

Outer sheath:			halogen-free, flame retardant compound

Cable overprint:			DIGITUS DK-1741-VH 4x2x23# S/FTP CATEGORY 7

SHIELDED LS0H CABLE VERIFIED to CAT 7 ISO/IE C-					11801 & IEC 61156-5 Tested to 1200MHz FR IEC 					60332-1 CE 2002/95/EC (RoHS) [Meter specification] 					METER

Color:				orange, RAL-2000

1200 MHz:

Average impedance:			100±5 Ohm @ 1-1200 MHz

Propagation speed:			75-77% nom.

Capacitance:				40 pF/m nom @ 1 KHz

Capacitance against ground:	1.6 pF/m max. @ 1 KHz Insulation Resistance	0.5 GOhm•Km min.

Insulation resistance:		72 Ohm/Km max. (2% max. resistance unbalance).

DC resistance:			147 Ohm/Km max. (2% max. resistance unbalance).

Operating voltage:			72Vdc max.

Insertion loss:			85dB min @ 30-100 MHz.

85-20Log(f/100) dB min. @ 100-1000 MHz.

PS-ANEXT:				92.5-15Log(f) dB min. @ 1-600 MHz (67dB max).

PS-AFEXT:				78.2-20Log(f) dB min. @ 1-600 MHz (67dB max.)

Phase delay:				534+36/f½  nS/100m max. @ f=1-1200 MHz.

Propagation delay:			25 nS/100m max.

Fire Behavior:

Non-flammability:			according to IEC 60332-3-24

Absence of Halogen:			according to IEC 60754-1/2

Smoke density:			according to IEC 61034-1/2

Fire load (KJ/m):			650 KJ/m (approximate value)

Chemical Properties:

Free of hazardous substances according to RoHS 2002/95/EG

Certificates and Approvals:

Seal of quality with production control: ETL mark

Link Performance: DIGITUS Cabling Systems DK and DN Design Series

Test Certificates: IEC 61156-5

LVD Compliance (73/23/EEC): CE mark

Product: DIGITUS

Type: DIGITUS CAT 7 S-FTP Twisted Pair Installation Cable

Item no. DK-1741-VH-xxx

or equivalent. When submitting a tender, the bidder has

to prove the equivalence by submitting the corresponding

data sheets/certificates from an independent testing institute:

Make/type offered:

Materials:............EUR

Wages    :............EUR

Fully delivered and installed

Piece              ...........EUR     ...........EUR