TEXT BLOCK

ASSMANN DIGITUS modular jack, DN-93612, RJ45, Category 6/6A, shielded

SPECIFICATIONS

------------------------------------------------------------------------------

OZ       Specification of Services                 Unit Price      Total Price

------------------------------------------------------------------------------

-.-.-	Shielded RJ45 Cat.6/Cat.6A Keystone Jack.

Housing made of high-gloss nickel-plated CuZn sheet.

Cover and area for strain relief and shield contact made of die-cast zinc.

Housing cover with embossed surface for improved surface feel.

Preparation of the cable connection takes place via an external cable sorter.

Interior color coding according to TIA/EIA 568 A/B.

Connection of insulated conductor by means of tool-free insulation displacement connection.

suitable for conductor diameter AWG 24 (0.4mm) up to AWG 22 (0.64mm).

Secure shield contact through wide contact area and separate strain relief through cable ties.

Suitable for combination with design covers of well-known manufacturers of switching material such as BUSCH-JAEGER; PEHA; JUNG; FELLER (CH).

Optional plug-on dust protection plug.

Length x Width x Height in mm (total)

- 41x18x24.

Die size – according to Keystone Standard 19.35x14.8 (height x width in mm).

Category 6 according to

ISO/IEC 11801:2009-04 , EN 50173-1:2002-09 , IEC 60603-7-5/Ed. 1.0 and

TIA/EIA 568 B.2-1 June 2002

Compliance with EMC directives according to EN 55022 Class B (radiation)

and 50082-1 (interference immunity)

Support of 10GBASE-T up to 500 MHz according to

- ISO 11801 Ed. 2.1 ClassEA Channel

Make/type:

DIGITUS CAT 6 Class EA Keystone Jack, shielded

Item no. DN-93612

or equivalent. When submitting a tender, the bidder has

to prove the equivalence by submitting the corresponding

data sheets/certificates from an independent testing institute:

Make/type offered:

Materials:............EUR

Wages    :............EUR

Fully delivered and installed

Piece              ...........EUR     ...........EUR