TEXT BLOCK

ASSMANN DIGITUS modular connector module, DN-93615, RJ45, Category 6/6A, shielded

SPECIFICATIONS

------------------------------------------------------------------------------

OZ       Specification of Services                 Unit Price      Total Price

------------------------------------------------------------------------------

-.-.-	Shielded RJ45 Cat.6/Cat.6A modular jack.

Housing, cover and area for strain relief and shield contact made of die-cast zinc with nickel-plated surface.

Preparation of the cable connection takes place via an external cable sorter.

Interior color coding according to TIA/EIA 568 A/B.

Connection of insulated conductor by means of tool-free insulation displacement

connection suitable for conductor diameter AWG 24 (0.4mm) up to AWG 23 (0.546mm).

360° shield contact through circumferential contact area and separate strain relief through cable ties.

Suitable for combination with design covers of well-known manufacturers of switching material such as BUSCH-JAEGER; PEHA; JUNG; FELLER (CH).

Flexible cable entry for secure adaption to the outer cable sheath diameter.	Optional plug-on dust protection plug.

Length x Width x Height in mm (total)

- 37x16x20.

Die size - according to Keystone Standard 19.35 x 14.8 (height x width in mm).

UL 94-0-FR4 multilayer PCBs.

Category 6A according to

ISO/IEC 11801:2002-09 , EN 50173-1:2002 , IEC 60512-27-100 (48B/2060/CD)

TIA/EIA 568 C.2-1 June 2002

Re-embedded tested

Compliance with EMC directives according to EN 55022 Class B (radiation)

and 50082-1 (interference immunity)

Support of 10GBASE-T up to 500 MHz according to

- TIA 568B.2-10 Cat.6A Channel

- ISO 11801 Ed. 2.1 ClassEA Channel

Make/type:

DIGITUS high performance CAT 6A modular jack, shielded

Item no. DN-93615

or equivalent. When submitting a tender, the bidder has

to prove the equivalence by submitting the corresponding

data sheets/certificates from an independent testing institute:

Make/type offered:

Materials:............EUR

Wages    :............EUR

Fully delivered and installed

Piece              ...........EUR     ...........EUR